## Slide 1
OPEN STUDIO Building Simulation
TECHNICAL ENVIRONMENTAL SYSTEMS
W18 ANDREA FOPPIANI
MELISSA MARTINOLI
DAVIDE MONTANARI
LISANA SHIDQINA

## Slide 2
GROUND FLOOR PLAN
TYPICAL 1ST & 2ND FLOOR PLAN
SPACE TYPE BREAKDOWN
BUILDING
WITH 40% WINDOW/WALL RATIO
BUILDING WITH OVERHANGS (EXCLUDING NORTH SIDE)
FLOOR PLAN & BUILDING DETAILS
OPEN OFFICE
OPEN OFFICE
OPEN OFFICE
OPEN OFFICE
BREAK ROOM
BREAK ROOM
STAIRS
STAIRS
TOTAL BUILDING AREA: 1125 M2

## Slide 3
MILAN
BANGKOK
TORONTO
OVERVIEW
HIGHEST ENERGY CONSUMED
Location, climate conditions, and energy consumption per location
43.6532° N, 79.3832° W
13.7563° N, 100.5018° E
45.4642° N, 9.1900° E
Max. temp: 31.2oC
Min. temp: -18.8oC
Max. temp: 37.2oC
Min. temp: 19oC
Max. temp: 33oC
Min. temp: -5.1oC

## Slide 4
NO HEATING,
BUT SIGNIFICANT COOLING NEEDED
MILAN
BANGKOK
TORONTO
ELECTRICITY
ENERGY USE
END USE
OPEN STUDIO RESULTS
HIGHEST HEATING NEEDED
MORE INTERIOR EQUIPMENT NEEDED
Different climates influence different aspects of the end use

## Slide 5
OPEN STUDIO RESULTS
MILAN – HVAC LOAD PROFILES
BANGKOK – HVAC LOAD PROFILES
TORONTO – HVAC LOAD PROFILES
ALTERNATING TEMPERATURE, ALTERNATING ENERGY NEEDS
CONSTANT HIGH TEMPERATURE & COOLING NEED
HIGHER TEMPERATURE DIFFERENCES, MOST HEATING NEEDED
Overall heating & cooling loads relating to the outdoor temperature in each location

## Slide 6
WALL SIMULATION PROFILES
TORONTO
WALL 1 : BASE CASE
WALL 2 : Base case + air layer and light concrete
WALL 3 : Base case + air layer and light concrete + second and third insulation layer
TOTAL SITE ENERGY: 953.90 GJ
R-VALUE: 7.55 FT2 * h * R / Btu
U-VALUE: 0.749 W / m2 * K
WINDOW U-FACTOR: 1.13 Btu / FT2 * h * R
TOTAL SITE ENERGY: 938.61 GJ
R-VALUE: 10.05 FT2 * h * R / Btu
U-VALUE: 0.562 W / m2 * K
WINDOW U-FACTOR: 1.13 Btu / FT2 * h * R
TOTAL SITE ENERGY: 923.05 GJ
R-VALUE: 17.62 FT2 * h * R / Btu
U-VALUE: 0.317 W / m2 * K
WINDOW U-FACTOR: 1.13 Btu / FT2 * h * R
Simulation on different wall types to overcome climatic problems.
43.6532° N, 79.3832° W
TOTAL SITE ENERGY: 953.90 GJ
R-VALUE: 7.55 FT2 * h * R / Btu
U-VALUE: 0.132 Btu / FT2 * h * R
WINDOW U-FACTOR: 1.13 Btu / FT2 * h * R
TOTAL SITE ENERGY: 938.61 GJ
R-VALUE: 10.05 FT2 * h * R / Btu
U-VALUE: 0.099 Btu / FT2 * h * R
WINDOW U-FACTOR: 1.13 Btu / FT2 * h * R
TOTAL SITE ENERGY: 923.05 GJ
R-VALUE: 17.62 FT2 * h * R / Btu
U-VALUE: 0.056 Btu / FT2 * h * R
WINDOW U-FACTOR: 1.13 Btu / FT2 * h * R
Max. temp: 31.2oC
Min. temp: -18.8oC

## Slide 7
WALL SIMULATION RESULTS - COOLING
WALL 1
WALL 2
WALL 3
36.5
36
35
COOLING CONSUMPTION DECREASES SLIGHTLY BETWEEN THE THREE WALLS.

## Slide 8
WALL SIMULATION RESULTS - HEATING
WALL 1
WALL 2
WALL 3
88
86
83
HEATING CONSUMPTION DECREASES NOTICEABLY BETWEEN THE THREE WALLS.

## Slide 9
TOTAL SITE ENERGY: 923.05 GJ
R-VALUE: 17.62 FT2 * h * R / Btu
U-VALUE: 0.317 W / m2 * K
CONCLUSION
WALL 3 : Base case + air layer and light concrete + second and third insulation layer
Wall 1
Wall 2
Adding air gap and extra insulation contributes to the resistance of the wall. The wall is able to retain more energy, and therefore lessen energy loss.
WALL 3 is an ideal solution for the specific location, however,
WALL 2 may be a good economical compromise between the three types of walls.
Wall 1
Wall 2